## Slide 1
Fleet Zero Emission Vehicle
and Equipment Specification Writing
Case Study
Clean Cities Sacramento
10/19/2023
Casey Fallon
Director, Purchasing, Warehouse & Fleet
Sacramento Municipal Utility District (SMUD)

## Slide 2: Sacramento Municipal Utility District (SMUD)
CleanPowerCity.org
* In 2020, SMUD’s power supply was more than 60% carbon free. SMUD has a goal to reach zero carbon in its electricity production by 2030.
2

## Slide 3: SMUD fleet overview
927
fleet assets
13%
“electrified”
5,413,708
miles annually
3% zero emission (165,000 miles)
$10M
investment
Total annual fleet capital

## Slide 4: Breakdown of our fleet
294
2,438,750 annual miles driven
Pickups & vans
93
993,097 annual miles driven
Bucket trucks
Chart: 
0%
electrified
30%
hybrid-electric
106
488,557 annual miles driven
Light duty
48%
electrified
68
327,711 annual miles driven
Heavy duty
0%
electrified
141
1,143,685 annual miles driven
Service trucks
4%
hybrid-electric
225
9,907 annual miles driven
Construction equipment
14%
electrified

## Slide 5: Key metrics
Chart: Zero Emission Miles Driven
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Electric Miles Driven (hybrids not included) | 2462 | 14625 | 39992 | 66974 | 52917 | 73043 | 106322 | 167850
Chart: Fuel Economy (MPG)
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023
Fuel Economy (MPG) | 7.4805 | 7.9531 | 8.5842 | 8.4376 | 9.0938 | 8.98 | 8.8033 | 9.0536

## Slide 6: Spec writing for ZEVs…
Spec Writing
Technical complexity
Demanding customers
Supply chain
Technology advances
Customize vs. standard
Regulatory compliance
Ambitious fleet goals

## Slide 7
Electrify SMUD’s Fleet by 2030
Meet End User Minimum Requirements (Keep The Lights On)
Cost Effective Solutions
Repeatable Process
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Problem Statement
Case Study – SMUD Security
Calculate Energy Usage
  Fuel Consumption
Utilized five months of data
  Idle Time
  Drive Time
Notes: BOSWORTH
[Problem Statement]
  Executive direction to electrify
  Director direction to electrify
  Keep the Lights On
    Meet end user’s requirements to effectively perform their job
    [As Fleet and as Fleet’s Engineers, we do not want to tell other departments how to do their job; we want to find solutions to problems]
  Identify gross polluters
    Idle time is a significant contribution to fleet emissions
    Security Highest idle time in SMUD
  Repeatable Process
    Create a process to aid with evaluating other workgroup’s vehicles.
    We don’t want this to be a one time process

## Slide 8
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Calculate Energy Usage
  Fuel Consumption
Utilized five months of data
  Idle Time
  Drive Time
Case Study – SMUD Security
Problem Statement
Electrify SMUD’s Fleet by 2030
Meet End User Minimum Requirements (Keep The Lights On)
Cost Effective Solutions
Repeatable Process
Test for Idle Consumption
  Standardized set of criteria
Ambient Temp., A/C, Radio, State of Charge
Notes: BOSWORTH
[Utilize Telematics] - Create a repeatable process
  Calculate energy usage based on fuel consumption to determine minimum battery size (Focus on fuel consumption rather than mileage)
  Five Months' worth of usable data using telematic [data from July 2023]
    Idle time
    Drive time

## Slide 9
Case Study – SMUD Security
Methodology
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Test for Idle Consumption
  Standardized set of criteria
Ambient Temp., A/C, Radio, State of Charge
Calculate Energy Usage
  Fuel Consumption
Utilized five months of data
  Idle Time
  Drive Time
JULY 2023
Vehicle | Idle Time | Drive Time [hr] | Idle Time % | gal/hr | gal/hr Drive | gal/hr Idle | Drive kWh/month | Idle kWh/ month | Drive kWh/ day | Idle kWh/Day | Total kWh/Day
1884S | 104 | 43 | 71% | 0.68 | 0.81 | 0.63 | 1,283 | 94 | 41 | 3 | 44
1887S | 78 | 15 | 84% | 0.76 | 1.72 | 0.57 | 946 | 70 | 31 | 2 | 33
1947S | 56 | 14 | 80% | 0.72 | 1.82 | 0.45 | 937 | 51 | 30 | 2 | 32
2046P | 43 | 59 | 42% | 0.84 | 1.05 | 0.55 | 2,258 | 38 | 73 | 1 | 74
4016S | 256 | 112 | 70% | 0.84 | 1.51 | 0.55 | 6,195 | 231 | 200 | 7 | 207
4017S | 203 | 85 | 70% | 0.74 | 1.39 | 0.47 | 4,324 | 183 | 139 | 6 | 145
4018S | 50 | 18 | 74% | 0.72 | 1.35 | 0.49 | 892 | 45 | 29 | 1 | 30
4019S | 165 | 77 | 68% | 0.82 | 1.43 | 0.53 | 4,037 | 149 | 130 | 5 | 135
4020S | 172 | 91 | 65% | 0.91 | 1.58 | 0.56 | 5,268 | 156 | 170 | 5 | 175
4021S | 365 | 168 | 68% | 0.82 | 1.50 | 0.51 | 9,262 | 329 | 299 | 11 | 309
Notes: BOSWORTH
[Test Data] with current EVs (to determine idle kW consumption)
  Ran a test with current inventory of Bolt EVs, ID.4, Leaf, Mach E, mimicking average idle time
  Consistent radio, air conditioner, state of charge, ambient temperature settings

## Slide 10
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
JULY 2023
Methodology
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Vehicle | Idle Time | Drive Time [hr] | Idle Time % | gal/hr | gal/hr Drive | gal/hr Idle | Drive kWh/month | Idle kWh/ month | Drive kWh/ day | Idle kWh/Day | Total kWh/Day
1884S | 104 | 43 | 71% | 0.68 | 0.81 | 0.63 | 1,283 | 94 | 41 | 3 | 44
1887S | 78 | 15 | 84% | 0.76 | 1.72 | 0.57 | 946 | 70 | 31 | 2 | 33
1947S | 56 | 14 | 80% | 0.72 | 1.82 | 0.45 | 937 | 51 | 30 | 2 | 32
2046P | 43 | 59 | 42% | 0.84 | 1.05 | 0.55 | 2,258 | 38 | 73 | 1 | 74
4016S | 256 | 112 | 70% | 0.84 | 1.51 | 0.55 | 6,195 | 231 | 200 | 7 | 207
4017S | 203 | 85 | 70% | 0.74 | 1.39 | 0.47 | 4,324 | 183 | 139 | 6 | 145
4018S | 50 | 18 | 74% | 0.72 | 1.35 | 0.49 | 892 | 45 | 29 | 1 | 30
4019S | 165 | 77 | 68% | 0.82 | 1.43 | 0.53 | 4,037 | 149 | 130 | 5 | 135
4020S | 172 | 91 | 65% | 0.91 | 1.58 | 0.56 | 5,268 | 156 | 170 | 5 | 175
4021S | 365 | 168 | 68% | 0.82 | 1.50 | 0.51 | 9,262 | 329 | 299 | 11 | 309
Notes: BOSWORTH

## Slide 11
Case Study – SMUD Security
Methodology
Change Management Opportunities
Cross Reference Available Vehicles With Data
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Minimum ten vehicles
Two 12 hour shifts
Lighting Package
Body Accessories
JULY 2023
Vehicle | Idle Time | Drive Time [hr] | Idle Time % | gal/hr | gal/hr Drive | gal/hr Idle | Drive kWh/month | Idle kWh/ month | Drive kWh/ day | Idle kWh/Day | Total kWh/Day
1884S | 104 | 43 | 71% | 0.68 | 0.81 | 0.63 | 1,283 | 94 | 41 | 3 | 44
1887S | 78 | 15 | 84% | 0.76 | 1.72 | 0.57 | 946 | 70 | 31 | 2 | 33
1947S | 56 | 14 | 80% | 0.72 | 1.82 | 0.45 | 937 | 51 | 30 | 2 | 32
2046P | 43 | 59 | 42% | 0.84 | 1.05 | 0.55 | 2,258 | 38 | 73 | 1 | 74
4016S | 256 | 112 | 70% | 0.84 | 1.51 | 0.55 | 6,195 | 231 | 200 | 7 | 207
4017S | 203 | 85 | 70% | 0.74 | 1.39 | 0.47 | 4,324 | 183 | 139 | 6 | 145
4018S | 50 | 18 | 74% | 0.72 | 1.35 | 0.49 | 892 | 45 | 29 | 1 | 30
4019S | 165 | 77 | 68% | 0.82 | 1.43 | 0.53 | 4,037 | 149 | 130 | 5 | 135
4020S | 172 | 91 | 65% | 0.91 | 1.58 | 0.56 | 5,268 | 156 | 170 | 5 | 175
4021S | 365 | 168 | 68% | 0.82 | 1.50 | 0.51 | 9,262 | 329 | 299 | 11 | 309
Notes: FREEMAN
We held multiple Workgroup Meetings
  Understand work practice and duty cycle
  Determine Minimum Specifications
    Substantial Lighting Package
    Radios
    Laptop Mobile Data Terminal
    Push Bumper
    Storage for safety equipment
    Ballistic Panels

## Slide 12
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Change Management Opportunities
Cross Reference Available Vehicles With Data
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
Wait for More Viable EV solution
Current State: 75% to 80% solution
Higher Risk to Operations
Minimum ten vehicles
Two 12 hour shifts
Lighting Package
Body Accessories
Notes: FREEMAN
[Solution Finding]
  Cross reference available vehicle battery size (usable battery) with required energy per day
  Utilize data to determine vehicle quantity – are more vehicles needed to meet equipment needs
    (2) 12 hours shifts
    Minimum 10 vehicles
  Look at service locations and charging feasibility (Worked in parallel with utilization data)
    Security operates throughout SMUD’s service territory and power generation facilities – Sacramento County, Solano County, and Eldorado County
  Use data to look at possible change management opportunities
    Underutilized vehicles – 1947S was not utilized because it “is a piece of junk”

## Slide 13
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Change Management Opportunities
Cross Reference Available Vehicles With Data
Wait for More Viable EV solution
Current State: 75% to 80% solution
Higher Risk to Operations
Lower Mile per Year
Daily Utilization
Duty Cycle
  Supervisor Vehicles
  Pool Vehicles
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
Vehicle | Battery [kWh]
Lightning SR | 98
Lightning ER | 131
Bolt EUV SSV | 65
Blazer SSV | 102
Silverado EV | 200
Notes: FREEMAN
[Final Decision]
  EV was not a valid solution
  75% Solution: Upfit requirements, daily utilization, EV availability, charging infrastructure (remote locations provide level 1 charging, if at all)
  Determination to proceed with Hybrid vehicles
    Reduce emissions while maintaining operational efficiency
  Additional Example: Meter/Elec tech Van
    Duty Cycle, average milage, upfit requirements (Aux A/C, export power)

## Slide 14
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
Lower Mile per Year
Daily Utilization
Duty Cycle
  Supervisor Vehicles
  Pool Vehicles
Additional Testing
Wait for More Viable EV solution
Current State: 75% to 80% solution
Higher Risk to Operations
      Hybrid Vehicles
Final Decision
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Problem Statement
EV FLEETS
Data Exists in Telematics
Telematics Highlight the Worst Offenders
Replacement Strategy – Simple First pass
Understand the Workgroup Needs/Wants
Sometimes the Data Doesn’t Exist Online
Notes: FREEMAN
[New Focus]
  Simple First Barrier: 250 Pickup trucks – First pass using TTM Average daily milage less than 100 miles, Maximum mileage less than 200 miles – simple barrier since we can not purchase trucks at this time and we don’t have the infrastructure to support all pickup trucks
  This first pass can be used for SUVs as well.
  Typical vehicles include: Supervisor Vehicles, Facilities Vehicles, and Pool Vehicles
    low utilization – miles, operating time, duty cycle

## Slide 15
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Problem Statement
EV FLEETS
QUESTIONS?
Lower Mile per Year
Daily Utilization
Duty Cycle
  Supervisor Vehicles
  Pool Vehicles
Data Exists in Telematics
Telematics Highlight the Worst Offenders
Replacement Strategy – Simple First pass
Understand the Workgroup Needs/Wants
Sometimes the Data Doesn’t Exist Online
Notes: Data Exists in Telematics – Formulate a plan to utilize the data
Sometimes the Data Doesn’t Exist Online – Test to gain rear world data
Telematics Highlight the Worst Offenders – Easy to identify high polluters
Replacement Strategy – Simple First pass to take a smaller bite out of a larger initiative
Understand the Workgroup Needs/Wants – This may be a significant barrier to electrifying a fleet requiring more than just a vehicle

## Slide 16
Case Study – SMUD Security
      Focus on Low Utilization
New Focus
Lower Mile per Year
Daily Utilization
Duty Cycle
  Supervisor Vehicles
  Pool Vehicles
      Focus on Low Utilization
New Focus
      Hybrid Vehicles
Final Decision
Solution Finding
Vehicle​ | AVE Total kWh/Day​
1884S​ | 46​
1887S​ | 27​
1947S​ | 16​
2046P​ | 64​
4016S​ | 187​
4017S​ | 104​
4018S​ | 82​
4019S​ | 139​
4020S​ | 124​
4021S​ | 244​
Average​ | 103​
      Telematics
      Test Data
      Workgroup Meeting
Methodology
Problem Statement
EV FLEETS
QUESTIONS?
QUESTIONS